## Slide 1
Pneumatics
Pneumatik
By Clifford Mayhew
St Helens College
Notes: This presentation is an introduction to the principles, production and use of air in manufacturing and other industries.

## Slide 2: Basic principles
Notes: In order to understand how we use air, we need to understand a few basic principles of the properties and measurement of air. The pressure and flow properties of air are the most important principles to take note of.

## Slide 3: Pressure Measurement
Notes: Pressure can be measured using either complete vacuum or atmospheric pressure as a reference. If vacuum is used as a reference, the pressure measurement is called absolute pressure. If atmospheric pressure is used as a reference, the pressure measurement is called gauge pressure. Gauge pressure is usually for pressure measurements.

## Slide 4: Pressure Measurement
1 Bar = 100Kpa = 100KNm-2 = 14.5 PSI
Notes: There are several pressure units. All modern pressure units are derived from the Newton and the metre. Pressure is defined as a force per unit area, using Newtons and metres this gives a measurement in Newtons per metre squared (Nm-2). 1 Nm-2 = 1 Pascal and 100000 Pascals (100 Kpa) = 1 Bar.

## Slide 5: Compression
The pressure inside a closed cylinder will increase as the volume decreases.
Notes: When the volume of a closed cylinder is reduced, the pressure inside the cylinder increases. This is called compression.

## Slide 6: Gas Law’s
For a constant temperature, the volume and pressure relationship will obey the law:
Pressure x Volume = Constant
(Boyle’s Law).
This means if volume halves, pressure will double.
If volume decreases by a factor of five, pressure will increase by a factor of five etc.
Notes: Boyle’s Law says that the increase in pressure due to the compression is inversely linear, i.e., as the volume decreases by a factor, the pressure will increase by the same factor. Boyle’s Law does not account for any pressure changes. Therefore, the law only holds true for for a fixed temperature.

## Slide 7: Pressure Properties of Air
Notes: If the temperature change is ignored, the pressure rise in the closed cylinder can be calculated as in the slide shown. This helps us to calculate and understand the principle of compressors, the devices which produce high pressure air.

## Slide 8: Flow Properties of Air
When air flows through a restriction or orifice, there is a drop in pressure.
The resulting output pressure is less than the input pressure.
When there is no air flow the pressure is the same regardless of the shape of the vessel. This is Pascal’s Law.
Notes: Pascal’s law tells us that when air is not moving, the pressure in a vessel is the same in all parts of the vessel, regardless of its shape. If P was two bars in the diagram, then the gauges would measure two bar, regardless of where the gauge is placed. However, when the air is allowed to flow, the pressure in the narrow section of the vessel will fall as the speed of the air increases. When the air reaches the open section once again, the air pressure is lower than when it entered the vessel at the ‘P’ end.

## Slide 9: Compressed Air Production Drucklufterzeugung
Notes: Any pneumatic system requires high pressure air in order to function. Compressors are used to compress the air and impart it with energy. This energy is released by pneumatic devices at a later stage in order to perform work.

## Slide 10: The Compressor Kolbenverdichter
The compressor uses the gas compression principle to produce high pressure air for pneumatic systems. There are many types of compressor. A common compressor is the piston type shown below.
Notes: The piston compressor shown in the slide, draws air into the cylinder via the one way valve as its piston is pulled down. On the up stroke of the piston, the one way intake valve is closed and the outlet valve opens. High pressure air is produced due to the compression in the cylinder. High pressure air can also be produced using screw and vane compressors.

## Slide 11: The Receiver Speicher Kessel
The receiver collects and stores the air from the compressor.
Notes: The air produced by the compressor is stored in a vessel called the receiver. The function of the receiver is to store the air for future use, to smooth pressure spikes and to allow water to fall out of the air to the bottom of the receiver where it can be drained.

## Slide 12: Air Dryer Lufttrocknung
The compression process produces a lot of water which is forced out of the compressed air. The water must be removed using a dryer.
Notes: The moisture content of air depends heavily on the temperature of the air. The higher the temperature of the air, the more moisture it holds. Cooling air causes it to form water droplets (condensation) since the cool air can no longer hold the same moisture content. The production of compressed air produces a lot of water because a large amount of air (and moisture) is concentrated into a smaller space (compression). The extra water in the smaller volume produces water. The water can be removed by cooling or by desiccant dryers.

## Slide 13: Air Distribution
The pipework from the compressor is run downhill. This also helps to drain water from the system.
Notes: The air produced by the compressor is distributed by the pipe-work around the factory to the points where it is required. The pipe-work is ran downhill in a further attempt to remove excess water from the system.

## Slide 14: The Distribution system
Notes: The connections to the full system can be seen in this slide.

## Slide 15: Pneumatic Valves Pneumatik Ventile
Notes: A pneumatically controlled machine uses pneumatic valves to control and direct the air in a manner which allows us to perform many manufacturing operations such as lifting, moving, pressing etc.

## Slide 16: Pneumatic Circuits
Pneumatic devices are used for machine control.
Actuating devices can be linear or rotary.
Valves can:
  Condition
  Regulate
  Restrict
  Direct
  Decide
Notes: The type of valve used depends on the function required. A directional control valve is required to move a linear actuator (cylinder) in and out. A regulator is required to lower the pressure of the air to a preset level.

## Slide 17: A Pneumatic Circuit
The circuit extends both cylinders in a sequence when the two push button switches are pressed together. The cylinders will stop when the stop push button alone is pressed.
Notes: Pneumatic symbols are used to describe the function of a circuit. Each symbol represents a valve or device function. The symbols are connected together to form circuits and sub circuits. For example, the five valves in the red box are connected together to create a stop/start system for the whole circuit.

## Slide 18: Components
The previous circuit contains a filter regulator lubricator unit (air delivery) which is connected to the mains air supply from the compressor.
Logic valves decide when the operation begins.
Control valves direct the air.
Restrictors control the speed of the cylinders.

## Slide 19: Symbols and Components
The following slides show some common
pneumatic devices and their symbols as used
on engineering drawings.
Notes: To understand a circuit function and schematic diagrams, one must have an understanding of the valves and symbols used in pneumatic systems.

## Slide 20: 2/2 Way Directional Control Valve 2/2 Wegeventil
The circuit symbol describes the operation of the valve.
Notes: The symbol in this slide shows a two port two position valve. There are two boxes with different symbols inside (two position valve). Each box is just a different representation of the valve. Looking at any one of the boxes gives an indication of the number of ports on the valve. In the left hand box, there are two ports, air would be allowed to pass through the valve in this position. The arrow indicates this. In the left hand box, the same two ports are shown as blocked. In this position, air is not allowed to pass.

## Slide 21: Symbol Operation
To see how the symbol works, consider the animation below.
Air is now allowed through the valve to the output.
Air is initially blocked from passing through the valve.
Notes: The animated slide above shows that one must imagine the valve symbol moving and the connections staying stationary. In this way we can see that in one position air is allowed to flow, and in the other position, air is blocked.

## Slide 22: 3/2 Directional Control Valve Normally Closed 3/2 Wegeventil Sperr Ruhestellung
A 3/2 valve allows exhaust air to vent to atmosphere in the ‘off’ position.
Notes: The three port two position valve in this slide allows air to pass in the left hand position and blocks in the right hand position. This function is similar to the 2/2 valve in the previous slide. The main difference with this valve is that any air trapped in the outlet of the valve is allowed the pass out of the exhaust port in the right hand position. This is a normally closed valve because the connections are drawn on the ‘air blocked’ side of the valve. This valve is commonly used for roller actuated ‘switches’.

## Slide 23: 3/2 Directional Control Valve Normally Open 3/2 Wegeventil Durchflu Ruhestellung
Notes: This is a normally open 3/2 valve because the connections are drawn on the ‘air pass’ side of the valve.

## Slide 24: 5/2 Directional Control Valve 3/2 Wegeventil
A five port valve switches the two output ports from exhaust/pressure to pressure/exhaust.
Notes: The five port two position valve can direct air to two outlet ports. When one port is delivering air, the other port is exhausting air. This valve is commonly used to direct air to actuating devices such as cylinders and rotary actuators. Mains air is connected to the middle port, the two end ports exhaust the air.

## Slide 25: Inside the 5/2 Valve
In this position, pressure is allowed from P to B. Exhaust from A to S.
In this position, pressure is allowed from P to A. Exhaust from B to R.
Notes: The spool inside the valve directs the air to the required port depending on the position signal (in this case Y or Z). When Y is operated, air will pass from P to B. Exhaust air will pass from A to S. When Z is operated, air will pass from P to A. Exhaust air will pass from B to R. If one examines this function and the schematic function on the previous slide one can see the similarities between valve function and schematic descriptions.

## Slide 26: Spool Operation
This animation shows the spool (schieber) operating when each pilot is operated.
Notes: The animation of this slide shows how the spool is moved by the pilot air signals to Y and Z.

## Slide 27: Cylinder
Also known as a linear actuator. This is the component that provides the movement to achieve the machine operation.
Notes: Linear actuators or cylinders are used to convert the energy in the air into a linear motion. The full name for this cylinder is a double acting, differential cushioned linear actuator. Double acting because it is pushes by air in and out. Differential because there is a different volume in the back and front of the cylinder. The cushion is indicated by the arrow and extra diameters on the rod. Cushioning the cylinder prevents excessive wear and noise.

## Slide 28: Cushion Operation
Notes: The diagram in this slide shows how the cushion traps air in the cylinder and forces it through a needle valve thus giving the cushion effect. The amount of cushioning can be adjusted by winding the adjusting screw in (heavier cushioning) or out (lighter cushioning).

## Slide 29: 5/2 Valve Operation
The animation shows the operation of a 5/2 DCV when connected to a differential cylinder.
In this position, pressure is connected to the front of the cylinder.
When the device is activated, pressure is switched to the back of the cylinder which now extends. Note that in both positions, air must be able to escape via the exhaust ports.
Notes: This animation will help you to understand how the valves and actuators are connected to perform a circuit function. In this case, the 5/2 valve is connected to a cylinder. As the valve is switched from one position to another, the cylinder is forced in or out by the air.

## Slide 30: Two Pressure Valve (AND) Zweidruck Ventil
An output is achieved when input 1 AND input 2 are activated.
Notes: This valve can be used to logically decide if there is move than one signal present on the inputs. We can use this information to determine if a part is in position AND and guard is down before we perform a clamping operation.
An alternative for this symbol is shown below.

## Slide 31: Shuttle Valve (OR) Wechselventil
An output is achieved when input 1 OR input 2 are activated.
Notes: The OR valve is used to decide if there is a signal from either of two sources. This can be used to provide a stop from two different positions for example.
An alternative symbol for the or is shown below.

## Slide 32: Pressure Regulator With Relief Port Druckregelventil mit Druckentlastung
The output pressure is regulated by the spring pressure.
Notes: The compressor produces high pressure air at a higher pressure than is normally required. This is to overcome pressure losses in the distribution system. A pressure regulator is used to lower the pressure for the system components. A pilot signal (the dotted line on the left hand side of the symbol) monitors the output pressure of the valve. The pilot pressure acts against a spring which is used to set the pressure.

## Slide 33: Inside the Regulator
Output pressure acts on the diaphragm against the spring.
Input pressure is allowed through the normally open valve.
When the output pressure is greater than the spring force the valve closes.
Notes: The regulator uses a diaphragm to open and close the valve under low and high pressure conditions. The diaphragm is opposed by the pressure setting spring.

## Slide 34: The Regulator in Action
Notes: This animation should help you to understand the operation of the pressure regulator. Note that excess pressure is vented via the bottom ports of the valve when the pressure is too high in the outlet.

## Slide 35: Filter Druckluftfilter
The filter is used to remove small particles from the air. If the particles are left in the air they will cause the pneumatic components to stick.
Notes: Filters are an essential component of the pneumatic system. Their function is to remove small particles from the air. If the particles in the air were allowed to remain, they would block small ports and jam spools etc. Note the diamond shape of the symbol. Symbols containing by a diamond are usually conditioning the air in some way.

## Slide 36: Inside the Filter
Air must pass through the filter in order to get to the outlet.
Water in the air is allowed to fall into the water bowl. The bowl must be drained regularly.
Output air is cleaner and drier.
Notes: This slide shows how air is forced through the filter element to the outlet of the filter. The filter element can be either a fibre or bronze element. Note that, since the air is travelling through an ‘open space’ it slows down. This allows any water in the air to fall out into the condensate bowl. This bowl must be drained periodically. Filters with automatic drains can be obtained, these use a float in the bowl to open a valve at a preset level.

## Slide 37: Lubricator Druckluftoler
The lubricator puts a mist of oil into the air. This lubricates the internal components of the pneumatic valves.
Notes: Some pneumatic components require lubrication. The conditioning unit in this symbol is a lubricator. Oil is drawn from a bowl and is introduced into the air as a mist.

## Slide 38: Inside the Lubricator
Air flows through the orifice causing a drop in pressure.
Oil is drawn from the bowl due to the pressure drop
Notes: The tube in the oil is indicated on the symbol as a small line:
The bowl must be ‘topped up’ regularly with oil to keep the pneumatic components lubricated. Not all components require lubrication. Many modern components, developed for the food industry must not be lubricated.

## Slide 39: Restrictions Drossel Blende
Restrictions are used to control the air flow to pneumatic devices. The speed of the pneumatic devices will therefore be controlled.
Notes: A restriction or throttle is used to control the flow of air in a pneumatic system. Without restrictions, the actuating devices would move too fast for certain applications.

## Slide 40: Non Return Valves Ruckschlagventil
Check valves are used to allow air in one direction only.
Notes: The check valve or non return valve is used to allow air to pass in only one direction. Air would be blocked when travelling from right to left, and would be allowed to pass when travelling from left to right.

## Slide 41: Flow Control With Check Valve Drossel Ruckschlagventil
By combining the restrictor and check valve, the air is restricted in one direction only.
Notes: The combination of a check valve and restrictor allows us to restrict air in one direction and free flow in the other direction. In this symbol air is restricted from left to right and will free flow from right to left.

## Slide 42: Inside the Restrictor and Check Valve
Air in this direction closes the check valve and is forced through the restriction.
Air in this direction opens the check valve. The restriction is now bypassed.
Notes: This slide shows the construction of the restrictor and check valve. The restriction is achieved using a needle valve. The check valve is constructed using a ‘flapper valve’.

## Slide 43: Valve Actuators
Many valves are actuated by some mechanical or electrical method. Below are some common actuation symbols.
Notes: The directional control valves we have discussed require switching in some way. There are many ways of actuating the valves, as indicated in this slide. Push buttons, solenoids and air are all very common methods of valve actuation. Push buttons and hand levers are used for manual operation. Solenoids and pilots are are switched indirectly from some other source, electrically in the case of a solenoid (by PLC for example) or by another valve in the case of a pilot.

## Slide 44: Pilot/Spring operation on a 5/2 Valve
Before the button is pressed, the spring holds the valve spool in the spring position.
When the button is pressed, the button force overcomes the spring force and the valve switches position.
Notes: This animation shows a 5/2 push button/spring actuated directional control valve. When the push button is not pressed, the spring forces the spool into a position which allows air to the left hand port. When the push button is pressed, air is directed to the right hand port.

## Slide 45: Simple Circuit Operation
Notes: This animated schematic of a cylinder being controlled in and out is an example of how one should imagine the circuit diagrams working. In this example, the back 3/2 roller actuated DCV (Directional Control Valve), switches the 5/2 DCV into a position which sends the cylinder out. The cylinder is then returned by the out 3/2 DCV.

## Slide 46: The Complete System
Notes: The complete system is shown in this slide. The compressor produces air, the receiver stores the air, the dryer dries the air. Distribution of the air is via the pipe-work, and the air is used in pneumatic circuits to manufacture many components.